qgSurf
Determination of intersections between Cartesian planes and raster digital elevation models
Algorithm Theoretical Basis Document

Start editing: 2018-11-25
Vers. 1.0 - last editing: 2018-11-29
Completed: No

The intersection between a geological plane and a topographic surface is of interest in geological field mapping and in structural geology.
The described approach is a generalization of the approach formerly used in qgSurf (and by extension in gsf). The previous requirements were more restrictive, assuming no grid rotation/skewing.
However, GDAL uses an affine tran sformation matrix as its “geotransform”, both grid rotation and skewing are theoretically possible (Fig. 1). A more general approach in qgSurf allows to correctly handle all theoretical cases, also those that in practice are rare.

Figure 1: Example of a regular orthogonal grid with an affine transformation applied.

Determination of plane-DEM intersections

Figure 2: Determination of intersecting plane (P points) and DEM (D points) along the j direction.
To solve this problem, its geometric domain is converted to a simplified 2D approach from its original 3D nature.
The basic operation is the determination of the intersection between two lines, representing the plane and the DEM in a specific direction. This direction will have two possible values: the raster i- and j- directions. At the end the two results are combined into a single solution, with the same dimensionality (i.e., points).
We have a plane-DEM intersection point (for instance between j=0 and j=1 in Fig. 2), when their relative position along the z-axis switches between consecutive cell centers. When, between two consecutive cell centers, the plane line is always higher (or lower) than a DEM line, there is no intersection (e.g., between j=1 and j=2 in Fig. 2).
Obviously, when at a cell center line and DEM points coincide, it is considered an intersection point.

augmented matrix