qgSurf
Determination of intersections between Cartesian planes and raster digital elevation models
Algorithm Theoretical Basis Document

Start editing: 2018-11-25
Vers. 1.0 - last editing: 2018-11-29
Completed: No

The intersection between a geological plane and a topographic surface is a subject of interest in geological field mapping and structural geology.
The approach implemented in vers. 2.0.0 of qgSurf solve this problem in a generalized way with repsect to the previous approach, that assumed no grid rotation or skewing.
The affine transformation matrix used in GDAL to implement its “geotransform”, allows to apply both rotation and skewing to a raster.
The GDAL geotransform can be represented by using an augmented matrix:

(1)

so that:

(2)

In eq. (1) we can substitute the explicit GDAL geotransform parameters:

(3)

The linear equations for the transformed coordinates are:

(4)

From the equation in (4), it can be easily observed that the gt0 and gt3 represent grid offsets in the x - and y- directions, respectively, gt1 and gt5 are scaling factors for x- and y- directions, while gt2 and gt4 represent rotations/skewing.
In the general case, an orthogonal grid can be transformed by a GDAL geotransform into a grid where x and y axes are no longer perpendicular (Fig. 1).

Figure 1: Example of an orthogonal grid transformed by an affine transformation.

Determination of plane-DEM intersections

To determine plane-DEM intersections, we consider the geometric intersections between lines representing the plane and the DEM surfaces. These lines correspond to the plane and DEM traces along two analyzed directions, parallel to the transformed i- and j- raster directions (i and j directions in Fig. 1).
Each of these directions is investigated separately, in order to derive the point intersections between lines, and the two resulting datasets are combined at the end, maintaining the 1D (i.e., point) nature.

As can be seen in Fig. 2, we have a valid plane-DEM intersection point between two consecutive cell centers (for instance j=0 and j=1 in Fig. 2), when the relative z positions of the line and the DEM traces switch between the two considered cell centers. On the other hand, when the plane line is always higher (or lower) than a DEM line, there is no intersection (e.g., j=1 and j=2 in Fig. 2).
Obviously, when at a cell center line and DEM points coincide, it correspond to an intersection point.

Figure 2: Determination of intersecting plane (P points) and DEM (D points) along the j direction.